## Slide 1: Practical rendering of detailed neuron simulations
Juan B. Hernando1, John Biddiscombe2, Bidur Bohara3, Stefan Eilemann3 and Felix Schüermann3
1Cajal Blue Brain (CeSViMa – UPM), Spain 2CSCS, Swiss National Supercomputing Center, Switzerland 3Blue Brain Project (EPFL), Switzerland
EGPGV, May 2013, Girona

## Slide 2: Outline
Background: The Blue Brain Project
  Simulating detailed cortical tissue
Motivations
Proposed solutions:
  RTNeuron
  Paraview + extensions
Experimental results

## Slide 3: The Blue Brain Project
The Blue Brain Project is the first attempt to systematically reverse engineer the human brain.
The goal is to build a facility in which simulation based research can be conducted to study the function and dysfunction of the brain.

## Slide 4: Simulating detailed cortical tissue

## Slide 5: Simulating detailed cortical tissue

## Slide 6: Motivations
Analysis bottleneck:
  Simulations can produce huge amounts of data (+100 GB for 10K neurons, 1 s biological time, single variable reported at 0.1 ms intervals)
  Scientists require flexible interactive exploratory visualization (> 10 fps for simulation playback)
Visual complexity
  Complex and entwined geometry.
  Transparency for focus+context visualization.
Rendering complexity
  Geometrical workload: >4,000 segments (from the reconstructions), ≈150,000 triangles
  uncommon aspect ratio.
  sub-pixel geometry.

## Slide 8
Notes: And this is how it looks like without transparency

## Slide 9: Motivations
Rendering complexity plus interactivity force to use parallelism to achieve the desired performance
There are 2 choices:
  Develop a custom solution.
  Reuse and adapt a readily available tool.
We have implemented and compared both.
Notes: Simplification and visual abstraction of the scene is another alternative, but we want to have the capability of showing the circuit “as is” during the exploratory analysis of a simulation.

## Slide 10: Ad hoc solution: RTNeuron
Based on Equalizer for parallel rendering
Features:
  On-membrane scalar variable visualization.
  Spike visualization.
  LODs.
  Dual depth peeling for transparency.
  Sort-firt, sort-last.
  Accumulation-based anti-aliasing when idle.

## Slide 11: RTNeuron: sort-first
Capsule skeleton-based view frustum culling executed in the GPU.
[Towards real-time visualization of detailed neural tissue models: view frustum culling for parallel rendering
Hernando et al, BioVis 2012]

## Slide 12: RTNeuron: sort-first

## Slide 13: RTNeuron: sort-last
Balanced kd-tree partition of the scene.
Each node builds only a portion of the tree.
View frustum code is reused to soft clip the meshes to the leaf box. If neuron geometries are unique the meshes can be hard clipped.
An OpenGL clip plane is set up for each leaf face.
Direct-send is used for parallel compositing of the final image. Z-buffer not transferred, only the compositing order.

## Slide 14: RTNeuron: sort-last
The k-d tree is built combining skeletal and mesh information.
Notes: The advantage of using the skeletons is that we can annotate the weights beforehand than then we don’t need to load the meshes, thus accelerating the loading phase.

## Slide 15: Off-the-self solution: ParaView
Neurons loaded, divided randomly amongst processes (to avoid layer imbalances)
Entire mesh partitioned using custom vtk+zoltan filter (NB. not neuron specific)
Each process renders piece using back to front depth sort
Final image composited in back-front ordered using node order KdTree
Mesh Partition Filter
Depth Sort
Painter
Compositor
KdTree
Passed via Extent Translator Information Key down pipeline

## Slide 16: ParaView Implementations
CPU
  Mappers : DepthSort (generates indices),
  PolygonMapper (renders by index)
GPU
  Piston Mapper (thrust),
    Compute distance (thrust::for_each)
    Depth sort - thrust:: sort_by_key
    Pass arrays directly to vtkgl::BindBuffer (&etc …)

## Slide 17: Experimental setup
10,000 neuron circuit with 1.4 × 106 triangles. 3 subcircuits for strong scaling: 1,000 neurons (14.5 × 106 tri) 2,000 neurons (30 × 106 tri) and 5,000 neurons (720 × 106 tri).
Two viewpoints (full view, close up) with opaque and transparent geometry, 1920 × 1200 resolution.
GPU accelerated rendering: Fat-node cluster (up to 6 nodes):
  Dual six-core 3.47GHz processors (Intel Xeon X5690)
  24 GB RAM
  3 GeForce GTX 580 each
  40 Gb/s QDR Infiniband interconnect
CPU only rendering: Cray XK7, 272 nodes of 2.1Ghz 16-core AMD Opteron.

## Slide 18: Rendered views

## Slide 19: Strong scaling in RTNeuron

## Slide 20: Strong scaling in Paraview
GPU acceletered rendering
CPU only rendering

## Slide 21: Weak scaling in RTNeuron

## Slide 22: Weak scaling in RTNeuron
400 neurons ≈ 5.6 × 106 triangles

## Slide 23: Conclusions
RTNeuron
Paraview
Pros
  Slighty faster.
  Better performance in close ups (thanks to VFC).
  More flexible.
  Faster pre-processing time.
Cons
  Less scalable.
  Non trivial implementation .
Pros
  Simpler implementation
  Very good scalability in CPU rendering mode
Cons
  Close up rendering less efficient due to the order between VFC and sorting steps.

## Slide 24: Future work
RTNeuron
  Sort-first like partitions in z-axis to reduce depth complexity.
  Dynamic load balancing in sort-last.
  Predictive dynamic sort-first.
  Improve transparency rendering in a single GPU.
Paraview.
  View frustum clipping before sorting.
  Fixing sorting artifacts.

## Slide 25: Questions?